## Slide 1: VTS Data Set Cleaning
Cleaning Process

## Slide 2: VTS Data Format
Input Data

## Slide 3: Raw Data Structure
One File for each Port and Day
File Format
  RecordID
  DateTime of Data Received
  PVT Data Packet
  IP Address
  Port#
PVT Data Packet
  1 to N PVT Records
PVT Record
  Start Character: $
  End Character: *
  Comma Separated fields in between

## Slide 4: Data Validations
#Records
  > 30
Start Character
  $
Packet Type :
  NR: Normal
  EA: Emergency Alert
  HP: Health Packet
  IN,IF: Ignition On and Off
  TA: Temper Alert
  BD, BR: Battery Disconnected/ Reconnected
  BL: Battery Low
  TS, TE: Trip Start and Trip End
  HA,HB,RT: Harsh Acceleration, Break, Rash Turn
Packet Status:
  L: Live
  H: History
IMEI
  15 Numeric
Latitude
  Float
Longitude
  Float
Date Time
  Valid
PDOP
  Numeric and < 10
Temper Alert
  C or O else put N

## Slide 5: VTS Data Output Format
Sr. No | Data | Type | Comments
1 | IMEI | String | Device Identification
2 | VendorID | String | Device Supplier
3 | VehicleNumber | String | Vehicle Registration Number
4 | MNO | String | Operator Name
5 | MCC | String | Operator Country Code
6 | MNC | String | Operator Code
7 | LAC | String | Location Code of Cell tower
8 | CellID | String | Tower ID
9 | PacketType | String | Normal, Emergency, Health, Ignition..
10 | PacketStatus | String | Live or History
11 | DateTime | DateTime | Packet Generated Date Time
12 | GPSFix | Numeric | 1 (No Error) and 0(Error)
13 | Lat | Numeric | Accuracy of 7 digits
14 | LatDir | String | N/S Direction
15 | Lon | Numeric | Accuracy of 7 digits
16 | LonDir | String | E/W Direction
17 | InstSpeed | Numeric | Instantaneous Speed
18 | Heading | Numeric | Direction in degrees
19 | Altitude | Numeric | Hight of the vehicle
20 | PDOP | Numeric | Goodness of GPS, normally <7 and Good accuracy means < 4
Sr. No | Data | Type | Comments
21 | Ignition | Numeric | 1 (On) 0 (off)
22 | MainPowerStatus | Numeric | 0 (Disconnected) 1 (Connected)
23 | EmergencyStatus | Numeric | < 0 (Missing) 0 (Normal) 1 (Emergency)
24 | TemperAlert | String | C (Cover Closed), O (Open)
25 | GPSSignalStrength | Numeric | Can be used to decide on struct on GPS data
26 | DigitalInput1 | Numeric | 0 or 1
27 | DigitalInput2 | Numeric | 0 or 1
28 | DigitalInput3 | Numeric | 0 or 1
29 | DigitalInput4 | Numeric | 0 or 1
30 | DigitalOutput1 | Numeric | 0 or 1
31 | DigitalOutput2 | Numeric | 0 or 1
32 | DigitalOutput3 | Numeric | 0 or 1
33 | DigitalOutput4 | Numeric | 0 or 1
34 | FrameNumber | Numeric | 000001 to 999999
Folder Containing one file for each IMEI

## Slide 6: Output Summary Data from Raw Data Extraction
Summary file for each Port and Day containing following fields
  Input FileName
  Total number of PVT Data Packets
  Total Number of PVT Records
  # Good PVT Records
  #Rejected PVT Records
Error file for each Port and Day containing following fields
  RecordID
  Port
  PacketIndex
  Error Description
  Original PVT Record
Good Record file for each Port and each day containing following Fields
  RecordID
  Original PVT Record

## Slide 7: VTS Data Cleaning Flow For Good PVT Records
Workflow Design

## Slide 8: Data Cleaning Workflow for each IMEI
Duplicate Removal
Same LatLong and Datetime
Remove Stationary Points
Improves RDP in future
Identify & Split Trips
If Ignition On/Off Available use it
Intermediate points with displacement < 35 Meters
Stopped for more than 360 Minutes or more than 30 less than 360 but speed < 5 Km/hr
Ignore Parked Points
Split GeoSpatialSeparated Segments in a Trip
Same Trip but vehicle moving in two Geographies
Remove Inconsequential Points
Modified RDP algorithm
Based on Spatial and Speed Deviation
Outputs in two folders
AllData: Containing all points with Remove and Comment flag
CleanData: Afer removing Remove points and Remove/Comment Columns

## Slide 9: Split GeoSpatialSeparated Segments in a Trip
Identify Discountinuities in the successive points
Find which earlier Segment it belongs
Check Other Segments other than Segment of Previous Point
If no Segment qualifies then give this point a new Segment number
Find Segment with which Speed < SpeedCutoff1 and Minimum Distance
If Time Difference is 0,
Distance < 35 Meter – Then remove as Stationary Point
Distance > 35 Meter then different Segment
Speed w.r.t previous point > SpeedCutoff2 (120KM) – Separate Segment
Speed > SpeedCutoff1 (119 KM) and < SpeedCutoff2 then distance > distCutoff (0.035KM) then Separate Segment

## Slide 10: Data Cleaning Summary Output
Clean Record summary file with following fields is created
  IMEI
  Duration in Days: End Date – StartDate + 1
  Total PVT Points
  Duplicate PVT Points
  Stationary PVT Points
  Total # Trips
  Total # Segments
  Total # RDP Excluded PVT Point
  Maximum PVT Points in a Segment across all trips
  Maximum time of the Segment across all trips
  Total Time of all the segments
  # Segments where Count of PVT Points <=3

## Slide 11: Demo of Clean Data
Screen Layout Design

## Slide 12: Summary Display
Start Date of Data
#IMIE
#Total PVT Points
Trip Distribution Table (Trip Count and #IMIEs)
  Trip Counts: 1-6, 7-10,11-20,21-30,31-50, > 50
Trip Time Distribution (Time and count of Trips)
  Time: <30 Min, 30Min-1.5Hr, 1.5Hr – 3Hr, 3Hr-6Hr, 6Hr – 10Hr, > 10Hr
Hour of Day Distribution (Trip Start Time and Count of trips)
  Start Time: Midnigh-4AM, 4AM-8AM, 8AM-2PM,2PM-6PM, 6PM-9PM, 9PM-Midnight
End Date of Data
#Used PVT Points
#Rejected PVT Points
Segment Distribution (Segment Count and #Trips )
  Segment Counts: 1, 2, 3, 4-6, 7-8, > 8
Trip Distance Distribution (Distance and count of Trips)
  Time: < 1KM, 1KM-10KM, 11KM-20KM, 20KM-40KM, 40KM – 60KM, > 60KM
Day of Week Distribution (For each Day count of Trips starting on that day)
  DOW: Mon to Sunday